# Text boxes

Passenger

Emergency

Checklist

Cirrus SR20

N84MR

- Follow my instructions; remain calm

- I will show you (front passenger) how to use the radio.

  - This is the “Push to Talk” button

Push it in to talk to the Air Traffic

Controller;  release it to hear the

response.   Talk slowly and clearly.

  - First try talking on the frequency currently in use.  Only if that doesn’t work, use the emergency frequency - 121.5

  - A quick way to select 121.5 is to press and hold this button for about 3 seconds;                                                      Do this on both radios.

  - Push 7-7-0-0 on these keys.

Make sure that 7700 shows in the display;  if not, repeat this step.

- Parachute – do NOT use unless pilot is incapacitated.

  - Shut the engine down by moving this lever all the way

toward the rear of the airplane.

  - Pull the safety pin from the parachute handle in the ceiling.

  - Pull the parachute deployment handle straight down with a steady pull.

  - Check that your seatbelts are secure.

  - Expect a hard  landing.

  - After landing, open the doors by moving the door handles up and back.

  - If the doors are jammed, remove the hammer from the lid of the center armrest. Use it to break open a window by hitting a CORNER of the window.

  - Move away from the airplane; walk upwind (into the wind).

- Equipment

  - Fire Extinguisher – under pilot seat

  - Flashlights, 2-Way Radio, GPS – Pilot or Front Passenger side pocket.

  - Hammer, Flashlights, Tools – Center armrest.

  - First aid kit (including compass, blanket, life vests) – Baggage compartment.

  - Batteries – Pocket at base of left rear passenger seat.

Mike Radomsky developed this checklist for his own use.  Other pilots may use this as is or adapt it.  In either case, they accept full and complete responsibility for the content and all consequences of use of this checklist.

Press 7-7-0-0 here (

(Check that 7700 appears in display.  If it does not, press 7-7-0-0 again.)

  - Radio - 121.5

  - Push-to-talk

  - Engine shutoff

- Equipment

  - Hammer

  - Fire Extinguisher

  - First Aid/Survival